## Slide 1: VR180 Overview
Hardware
Platform (OS)
Camera App
VR180 Media
Open formats (video, photo)
VR180 camera
Supported by Google Apps

## Slide 2: Hardware
130°x100° - 180°x180°
15+ resolved pixels per degree
Fixed focus at hyperfocal distance
6-axis IMU aligned with camera for VR stabilization
Interpupillary distance apart (64mm)
Synchronized frame exposure

## Slide 3: Platform / OS
QCS605 used for Google’s reference implementation
  Virtual stereo camera through Android Camera2 API
  Full capability for frame exposure control
  Real timestamps for synchronizing with IMU data.
Left camera
Right camera
Virtual camera
IMU
R
L
R
L

## Slide 4: Google’s Open-source Camera App
Hardware
WIFI/BT camera API
Platform
Stereo camera
Open-source camera app:
Sensor fusion;
Photo/video formats;
RTMP live streaming;
Integration with the VR180 companion app;
Simple customization API for new cameras.
Android API
IMU
Audio
VR180 companion app
Hardware/platform calibration & VR metadata

## Slide 5: Calibration & Validation
Run calibration toolkit
Every device should be factory-calibrated to produce accurate VR180 media
  Calibration toolkit is provided for producing necessary VR metadata
  Validation toolkit is also provided for verifying the output VR180 media
  More instructions can be found in the released toolkits.
IMU/camera time offset
Camera App in calibration capture mode
Time-offset calibration
Lens calibration
Lens parameters & metadata
Camera App ready for regular capture mode
Capture in calibration boxes
Calibration datasets